907.2 Hazardous Material Construction Guidelines

This document shall be distributed at all Pre-Construction Conferences.

General Contractors and all subcontractors engaged in construction projects administered DFMS shall adhere to the following general guidelines pertaining to hazardous materials. These guidelines do not in any way relieve the contractor of his responsibilities imposed by regulatory agencies such as OSHA and EPA.

- At the preconstruction meeting, the Project Manager shall provide the Contractor with copies of all known surveys, sample results, reports, and any other information identifying hazardous materials within the project area. If such information exists, the Contractor (s) shall familiarize himself with the types and locations of the hazardous materials.

- If asbestos, PCB or similar materials must be disturbed during the performance of the contract work; the Contractor shall notify the Project Manager. The Project Manager shall have the responsibility of notifying the Hazardous Materials Coordinator and securing qualified abatement contractors to remove, or render harmless, the material affected by the work. The Contractor shall do no work in the affected area until such abatement has been accomplished. The Contractor shall not be required to perform any work relating to asbestos or polychlorinated biphenyl (PCB).

- If lead based paint (0.5% by weight) is identified on material to be scraped or drilled, the Contractor shall notify the Project Manager. The Project Manager shall have the responsibility of notifying the Hazardous Materials Coordinator to arrange for the abatement of the material. The Contractor shall not be required to perform work categorized as lead paint abatement. Material containing lead required to be demolished may be treated as normal construction debris.

- If information concerning the presence of hazardous material does not exist, the Project Manager shall arrange for the Hazardous Materials Coordinator to conduct an inspection of the project and identify all materials considered to be potentially hazardous. These materials shall not be disturbed until they are determined to be non-hazardous. If materials are found to be hazardous then the Hazardous Materials Coordinator and the Project Manager shall arrange for abatement.

2.	Familiarize yourselves with Article No. 13 of the General Conditions which states the following:

Article 13 - Protection of Work, Property, Employees and Public

Hazardous Materials. In the event the Contractor unexpectedly encounters on the site material reasonable believed to be asbestos, polychlorinated biphenyl (PCB) or other classified hazardous substances/materials which have not been rendered harmless, the Contractor shall immediately stop work in the area affected and report the condition to the DFMS and Architect in writing. The work in the affected area shall not thereafter be resumed except by written agreement of the DFMS and Contractor if in fact the material is asbestos, polychlorinated biphenyl (PCB), or other classified hazardous substances/materials which have not been rendered harmless. The work in the affected area shall be resumed in the absence of any classified hazardous substances/materials or when it or they have been rendered harmless, by written agreement of the DFMS and Contractor.

- In instances when both asbestos containing and non-asbestos containing building materials of the same type (such as pipe fittings) have been identified, all such materials should be treated as potentially asbestos containing until tested and proved otherwise.

3.	In the event the Contractor should accidentally disturb material during the course of the work that is known to contain asbestos or is thought to potentially contain asbestos, he should immediately do the following:

Vacate and isolate the area. Post warning signs.

- Notify the Project Manager so he may contract with a qualified abatement contractor to ascertain if the material is asbestos and to clean and decontaminate the area.

4.	DFMS, University Departments, and the Contractor shall comply with the requirements of the OSHA Hazard Communication Standards (29 CFR 1910.1200).

A list of the hazardous chemicals to which the Contractor’s employees may be exposed shall be provided to the Contractor by the University Department Representative.

The Contractor shall provide the Project Manager and the University Department Representative with list of any hazardous chemicals they will bring on the job site.

5.	If during the Work hazardous materials are encountered, disturbed, or released, the Contractor shall contact each of the following persons as soon as possible:

Architect-Engineer:

Phone: ____________________

Fax:    ____________________

Email:   ____________________

University Department Representative:

Phone: ____________________

Fax:    ____________________

Email:   ____________________

Project Manager:

Phone: ____________________

Fax:    ____________________

Email:   ____________________

Received on behalf of Contractor:

Signature:		____________________

Printed Name:    	____________________